Chapter 13

Tactical Ventilation

Lesson Goal

After completing this lesson, the student shall be able to apply tactical ventilation knowledge and practices following the policies and procedures set forth by the authority having jurisdiction (AHJ).

Objectives

Upon successful completion of this lesson, the student shall be able to:

1.	Describe reasons for tactical ventilation. [NFPA® 1001, 5.3.11]

2.	Identify considerations that affect the decision to ventilate. [NFPA® 1001, 5.3.11, 5.3.12]

3.	Explain the critical fire behavior indicators present during tactical ventilation. [NFPA® 1001, 5.3.11]

4.	Define horizontal and vertical ventilation. [NFPA® 1001, 5.3.11]

5.	Explain the means for achieving horizontal and vertical ventilation. [NFPA® 1001, 5.3.11, 5.3.12]

6.	Describe the types of horizontal ventilation. [NFPA® 1001, 5.3.11, 5.3.12]

7.	Describe the types of vertical ventilation. [NFPA® 1001, 5.3.11, 5.3.12]

8.	Recognize other types of ventilation situations. [NFPA® 1001, 5.3.11]

9.	Explain the effects of building systems on tactical ventilation. [NFPA® 1001, 5.3.11, 5.3.12]

10. 	Ventilate using mechanical negative pressure in a window. [NFPA® 1001, 5.3.11, 5.3.12; Skill Sheet 13-I-1]

11.	Ventilate using mechanical negative pressure in a doorway. [NFPA® 1001, 5.3.11, 5.3.12; Skill Sheet 13-I-2]

12.		Ventilate using mechanical positive pressure. [NFPA® 1001, 5.3.11, 5.3.12; Skill Sheet 13-I-3]

13.	Perform horizontal hydraulic ventilation. [NFPA® 1001, 5.3.11, 5.3.12; Skills Sheet 13-I-4]

14.	Demonstrate the procedure for sounding a roof. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-5]

15.	Ventilate using a rotary saw to cut an opening. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-6]

16.	Ventilate using an axe to cut an opening. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-7]

17.	Demonstrate the procedure for opening a flat roof. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-8]

18.	Perform the steps for opening pitched roofs. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-9]

19.	Demonstrate the procedure for making a trench cut using a rotary saw. [NFPA® 1001, 5.3.12; Skill Sheet 13-I-10]

Instructor Information

This is the lesson covering tactical ventilation. This lesson covers types of ventilation, reasons for ventilation, and considerations that should be taken into account when performing ventilation. The lesson also covers the effects of building systems on tactical ventilation.

Important instructor information is provided in shaded boxes throughout the lesson plan. Carefully review the instructor information before presenting the lesson.

This lesson includes ten skill evaluation checklists that assess student ability to perform tactical ventilation. These checklists will allow students to meet the requirements of learning objectives 10-19.

Methodology

This lesson uses lecture, discussion, and skills practice. The level of learning is application.

Outline Contents

| Section | Outline Pages | Text Pages |
| --- | --- | --- |
| Section I: Reasons for Tactical Ventilation | 6 | 732 |
| Section II: Considerations Affecting the Decision to Ventilate | 11 | 734 |
| Section III: Types of Tactical Ventilation | 26 | 742 |
| Section IV: Effects of Building Systems on Tactical Ventilation | 65 | 763 |
| Section V: Skill Sheets | 68 | 765 |
| Section VI: Summary and Review | 73 | 764 |

Audiovisuals

Visuals 13.1 to 13.98 (PowerPoint® Presentation)

Easel pad and marker, optional

Evaluation

Chapter 13 Quiz

Chapter 13 Test

Skill Evaluation Checklists 13-I-1 to 13-I-10

Presentation Tools

Interactive Objects allow instructors to present information a piece at a time by clicking on hot spots in a larger image.

Each object is labeled in the Lesson Outline and indicated in the PowerPoint® presentation by a RED arrow in the top left corner of the image. This lets instructors know to use the mouse to explore all of the information on the slide.

After all of the information is displayed a reset arrow will appear in the bottom right corner of the image. Instructors can use this to remove the text and quiz students on content just covered or simply move on to the next slide.

To move to the slide after an interactive object, select the Click for next slide arrow on the left side of the slide.

Videos are used as discussion starters or to illustrate a concept or process discussed in the chapter.

These are labeled in the Lesson Outline and indicated in the PowerPoint® presentation by the Click image to play arrow on the left side of the slide.

Section I:	Reasons for Tactical Ventilation

# Reasons for Tactical Ventilation

pp. 732-734	Objective 1 — Describe reasons for tactical ventilation.

## Reasons for Tactical Ventilation

### Traditional term ventilation; more accurate tactical ventilation

### Planned, systematic, coordinated removal from a structure of

#### Heated air

#### Smoke

#### Gases

#### Other airborne contaminants

### Replace with cooler, fresher air for

#### Life safety

#### Incident stabilization

#### Property conservation

### Performed only when fire attack hoselines and teams in place, ready to advance

### Success depends on

#### Careful planning

#### Knowledge of building construction

#### Knowledge of fire behavior

#### Systematic application of procedures for removing the contaminants

#### Coordination with other fireground activities

### General reasons for performing

#### Reducing interior heat levels

#### Decreasing rate of fire spread

#### Reducing potential extreme fire behavior

#### Improving interior visibility

#### Improving firefighter efficiency

#### Improving victim survival potential

#### Reducing smoke damage and property damage

### Correctly implemented achieve incident priorities

#### Life safety

#### Incident stabilization

#### Property conservation

### Improperly applied – Results can be traumatic

#### Occupants

#### Firefighters

#### Physical structure itself

Instructor Note: Discuss with students “The Effect of Fresh Air on an Oxygen Deprived Environment” on pp. 733 of manual.

Discuss why it is important to effectively manage the introduction of fresh air.

## Life Safety

### Highest incident priority – Applies to

#### Occupants who may be trapped in structure

#### Firefighters who must enter it to locate, rescue them

### Tactical ventilation improves life safety for firefighters, occupants by

#### Increasing oxygen concentration

#### Reducing concentration of toxic products of combustion

#### Reducing temperature

#### Increasing visibility to aid in operations

#### Creating smoke-free paths of egress

## Incident Stabilization

### Tactical ventilation can be effectively combined with fire attack to stabilize incident

### Controlling and extinguishing fire – Accomplished in stages

#### Locating fire

#### Confining fire to room, area, or structure of origin

#### Extinguishing fire

## Property Conservation

### When smoke, gases, heat are removed from burning structure, fire can be confined to specific area

### If sufficient personnel on scene, salvage operations can begin outside immediate area of fire while fire control operations being conducted

### Tactical ventilation – Increases speed by which you can extinguish interior fires

#### Reduces fire damage in structure

#### Less water will be needed – Less damage to structure, contents

Review Question: What are the reasons for tactical ventilation? 
See pages 732-734 of the manual for answers.

Section II: Considerations Affecting the Decision to 
Ventilate

# Considerations Affecting the Decision to Ventilate

pp. 734-742	Objective 2 — Identify considerations that affect the decision to ventilate.

Objective 3 — Explain the critical fire behavior indicators present during tactical ventilation.

NOTE: The incident commander (IC) will make the decision to ventilate the structure.

## Risks to Occupants and Firefighters

### Occupants – Life hazards

#### Generally lower if the occupants are awake

#### If occupants were asleep when fire developed and are still in building, possibilities

##### May have been overcome by smoke and fire gases – some may still be alive; others may have perished

##### Might have become lost in the structure

##### May be alive and taking refuge in their rooms because the doors were closed

### Firefighters – Hazards expected from accumulation of smoke, fire gases

#### Visual impairment caused by dense smoke

#### Lack of oxygen

#### Presence of toxic gases

#### Presence of flammable gases

#### Possibility of rapid fire development

## Building Construction

### Single-family residential – Drastically changed over past 50 years

#### Structure – Increased over 150 percent between 1973 - 2008

#### Lot sizes – Decreased 25 percent

##### Reducing firefighter access

##### Increasing potential exposure risks

### Residential interior layouts, construction materials changed

#### Older structure construction

##### Composed of smaller compartments

##### Windows that could be opened for ventilation

##### Empty wall cavities that depended on air pockets to provide insulation

#### Modern single family structure features

##### Open floor plans

##### High ceilings, atriums

##### Lightweight manufactured structural components

##### Sealed windows

##### Wall cavities filled with synthetic insulation

#### Construction materials, interior finish of synthetic materials, light composite wood components

##### Add to fuel load of structure

##### Contribute to creation of toxic gases during fire

##### Energy efficient designs tend to contain fires for longer period of time – Creating fuel rich environment

##### Problems magnified in large-area residential structures

### Commercial, institutional, educational, multi-family residential structures rely on energy conservation measures that

#### Increase intensity of fire

#### Make use of tactical ventilation difficult

### Open plan commercial structures have

#### High fuel loads in contents

#### No physical barriers preventing spread of fire and smoke

### Use of plastics, other synthetic materials dramatically increased fuel load in all types of occupancies

#### Produce large quantities of toxic, combustible gases

#### Heat generated escalates rapidly - Can reach extreme temperatures

### Knowledge of building involved is an asset when decisions concerning tactical ventilation made; can be obtained from

#### Preincident plans

#### Inspection reports

#### Observation of similar types of structures

### Building characteristics to be considered

#### Occupancy classification

#### Construction type

#### Floor area and compartmentation

#### Ceiling height

#### Number of stories above and below ground level

#### Number and size of exterior windows, doors, other wall openings

#### Number and location of staircases, elevator shafts, dumbwaiters, ducts, roof openings

#### External exposures

#### Extent to which building is connected to adjoining structures

#### Type, design of roof construction

#### Type, location of fire protection systems

#### Contents

#### Heating, Ventilation, Air Conditioning (HVAC) system

## Fire Behavior Indicators

### Smoke – Observations can help obtain a clear picture of interior fire conditions

#### Volume of smoke discharge

#### Location of smoke discharge

#### Smoke color, density, pressure

#### Movement of smoke

### Air flow – Movement of air toward burning fuel and movement of smoke out of the compartment

#### Indicators of air flow

##### Velocity

##### Turbulence

##### Direction

##### Movement of neutral plane

#### Air flow caused by

##### Pressure differentials inside and outside compartment

##### Differences in density between hot smoke and cooler air

#### Air flow follows flow path

##### Parts – Inlet vent (where air enters), flow path, outlet or exhaust vent

##### Example – Single open doorway to structure fire

###### Air inlet is lower portion of doorway – Low pressure below neutral plane

###### Smoke exhaust is upper portion of doorway – High- pressure area above neutral plane

##### Other example

###### Air inlet – Entire open doorway

###### Smoke exhaust – Roof vent

##### Flow path is connection between inlet and outlet

### Heat

#### Visual indicators

##### Blistering paint

##### Bubbling roofing tar

##### Crazed glass

#### Thermal imager or infrared sensor – Scanning buildings with can provide data on internal temperature differences

#### Determine presence of increased temperatures through touch, feel on skin even at a distance

### Flame

#### Visible – Provides indication of size and location of fire

#### Effect or lack of effect of fire streams – Indicates size and extent of fire

#### Visible from outside structure – Allows flame indicator assessment along with ventilation, air flow

CAUTION: Do not rely solely on the presence or location of flames to assess an incident.

Review Question: How do smoke, air flow, heat, and flame impact fire behavior in a structure? 
See pages 737-738 of the manual for answers.

## Location and Extent of the Fire

### First arriving units must quickly determine fire size, extent, location

### Creating tactical ventilation openings in uncoordinated manner can spread fire to uninvolved areas, cut off occupant escape routes

### Severity and extent of fire – Dependent on factors

#### Type of fuel

#### Amount of time it has been burning

#### Activation of fire detection and suppression systems

#### Degree of confinement

### Phases and burning regime to which fire has progressed – Primary consideration in determining tactical ventilation procedures

## Type of Ventilation

### To be safe and effective tactical ventilation must be coordinated with other tactical operations

### Before orders given

#### IC must consider effects on fire behavior

#### Fire attack crews with charged hoselines, search and rescue teams, and exposure protection must be in place

### IC determines if ventilation is necessary – When, where, in what form should it be initiated

### Conditions upon arrival influence ventilation decisions

#### Incidents may simply require locating and extinguishing fire, ventilating afterward to clear residual smoke from structure

#### Other incidents require immediate ventilation to enable firefighters to enter building to conduct search and rescue, fire suppression operations

### Type and means of ventilation must be appropriate for situation

### Tactical ventilation must be capable of exhausting volume of heat, smoke, toxic gases produced by fire

## Location for Ventilation

### Before selecting place – Gather as much information about fire, building, and occupancy

### Factors that have a bearing on where to ventilate

#### Location of occupants

#### Availability of existing roof openings which access fire area

#### Location of the fire

#### Desired air flow path

#### Type of building construction

#### Wind direction

#### Extent of progress of fire

#### Condition of building and its contents

#### Indications of potential structural collapse

#### Effect ventilation will have on fire

#### Effect ventilation will have on exposures

#### State of readiness of fire attack crews

#### Ability to protect exposures prior to ventilating structure

#### Protecting means of egress, access

## Weather Conditions

### Building openings allow atmosphere to affect what happens inside building

### Conditions that affect ventilation

#### Temperature

#### Atmospheric pressure

#### Precipitation

#### Relative humidity

#### Wind

### Wind – Most important influence

#### Conditions must always be considered to determine proper means, location of ventilation in structures

#### Wind can blow the fire toward an external exposure, supply oxygen to the fire, or blow the fire into uninvolved areas of the structure

#### Means selected should work with prevailing wind, not against it

CAUTION:  A strong wind can overpower the natural convective effect of a fire and drive the smoke and hot gases back into the building.

## Exposures

### Internal – Building occupants, contents, uninvolved rooms/portions

#### Routing of smoke

##### When ventilation does not release heat and smoke directly above fire, routing of smoke is necessary

##### Routes smoke, heated fire gases travel to exit building may be same that occupants need to evacuate, firefighters need for working

#### Ventilation that causes heat, smoke, and fire to be discharged through wall openings below the highest point of building creates danger

##### Rising gases will ignite portions of building above exhaust point

##### Heat and fire gases may be drawn into open windows or attic vents

##### Heat and fire gases may ignite eaves of the building or adjacent structures

### External – Structures located adjacent to fire, affected by radiation and direct flame content

#### Window-mounted air conditioning units or HVAC intake vents

#### Nearby structures, vegetation can be ignited by convection

#### Fire drawn into exterior windows or openings

## Staffing and Available Resources

### Ventilation requires

#### Personnel

#### Resources

### Staffing requirements range

#### Two firefighters

#### Multiple companies

### Small structure, ventilation may only require two firefighters

#### Open doors and windows

#### Allow fresh air to enter and smoke to exit

### Ventilation may require additional personnel and companies when it is necessary

### Resources needed for tactical ventilation

#### Forcible entry tools

#### Power saws

#### Fans or blowers

#### Smoke ejectors

#### Flexible ducts

#### Stacking and hanging devices

#### Other support systems

#### Electrical power cords

#### Generators

### As amount and size of ventilation equipment increases, the space on apparatus to store and transport it will increase

Review Question: What considerations will affect the decision to ventilate?
See pages 734-742 of the manual for answers.

Section III: Types of Tactical Ventilation

# Types of Tactical Ventilation

pp. 742-744	Objective 4 — Define horizontal and vertical ventilation.

Objective 5 — Explain the means for achieving horizontal and vertical ventilation.

## Types of Tactical Ventilation

### Horizontal – Any technique by which heat, smoke, and other parts of combustion are channeled horizontally out of a structure by way of existing or created horizontal openings such as windows, doors, or other openings in walls

### Vertical – Ventilating at a point above the fire through existing or created openings and channeling the contaminated atmosphere vertically within the structure and out the top

#### Cutting a hole in roof above fire or opening existing roof access doors, scuttles, skylights

#### Requires horizontal inlet opening at or below level of fire

## Means to Accomplish

### Natural horizontal ventilation

#### Opening doors, windows to allow natural air currents and pressure differences to move smoke, heat out

#### Uses buoyancy of heated smoke and gases to draw them out through roof openings while entraining (pulling or drawing) fresh air into structure

### Mechanical horizontal ventilation

#### Uses fans, blowers, smoke ejectors

#### Most often used for horizontal – May be applied to vertical

#### Means involve pulling smoke, fire gases out through an opening or pushing fresh air into structure and displacing smoke, fire gases

### Hydraulic ventilation

#### Uses spray nozzle set on fog pattern to draw smoke out opening

#### Requires firefighters to operate nozzle within contaminated atmosphere

#### Disadvantage – Increased water damage to structure if done improperly

### Indicators for mechanical or hydraulic ventilation

#### Location and size of fire have been determined

#### Layout of building not conducive to natural ventilation

#### Natural ventilation slows, becomes ineffective and needs support

#### Fire burning below ground in structure

#### Involved area within compartment so large natural ventilation inefficient

#### Type of building or fire situation dictates its use

Review Question: What are the basic means used to accomplish ventilation?
See pages 742-744 of the manual for answers.

pp. 744	Objective 6 — Describe the types of horizontal ventilation.

## Horizontal Ventilation – Apply to

### Buildings in which fire has not involved attic or cockloft area

### Involved floors of multistoried structures below top floor, or top floor if the attic is uninvolved

### Buildings so weakened by fire that vertical ventilation is unsafe

### Buildings with daylight basements

### Buildings in which vertical ventilation is ineffective

## Natural Horizontal Ventilation

### Should work with existing atmospheric conditions, taking advantage of natural air flow

### Requires no additional personnel or equipment to set up, maintain

### When directed by IC

#### Create exit point first by opening windows, doors on leeward side of structure

#### Next – Openings on windward side of structure opened to permit fresh air to enter; forcing smoke toward exhaust openings

### Only single opening – Vent will serve as both inlet for air and exit for smoke

## Mechanical Horizontal Ventilation

### Necessary when natural flow of air currents and currents created by fire insufficient to remove smoke, heat, fire gases

### Negative-pressure ventilation (NPV)

#### Oldest type of mechanical ventilation

##### Smoke ejectors used to expel, pull smoke from structure by developing artificial air flow or enhancing natural ventilation

##### Smoke, fire gases drawn out of structure, fresh air drawn in by fans

#### Fan/smoke ejector placement

##### Placed in windows, doors, roof vent openings to exhaust smoke, heat, gases to exterior

##### Position in openings on leeward side to exhaust in same direction as prevailing wind – Creates lower pressure at inlet allowing fresh air to replace expelled air

Instructor Note: This information correlates with Skill Sheets 13-I-1 and 13-I-2. More information is found at the end of this lesson outline.

##### Properly seal open areas around to prevent air recirculation back into structure

###### Atmospheric pressure pushes air back through open spaces in doorway or window, pulls smoke back into room

###### Recirculation reduces efficient ventilation

###### Prevent by covering open area around fan with salvage cover or other material

##### Flow of smoke, gases to exhaust opening

###### Should be kept as straight as possible

###### Every corner causes turbulence, decreasing efficient ventilation

###### Smoke, gases accumulate near ceiling - Ejector should be located near top of opening

##### Avoid opening windows or doors near smoke ejector — Reduces efficient ventilation

##### Remove obstacles that reduce airflow

##### Do not allow intake side of smoke ejector to become obstructed by debris, curtains, drapes — May decrease amount of intake air

#### Selection and use

##### In potentially flammable atmospheres — Use those equipped with intrinsically safe motors, power cable connections

##### Must be turned off when moved, carried by handles provided

##### Before starting make sure

###### No one near blades

###### Clothing, curtains, draperies are not in a position to be drawn into fan blades

##### Avoid air discharged from fan — May contain debris

### Positive-pressure ventilation (PPV) – Technique using high-volume fan to create slightly higher pressure inside structure than outside

#### When pressure higher inside building, smoke forced through openings to lower-pressure area outside

#### Requires good fireground discipline, coordination, tactics

Instructor Note: Discuss with students the Information Box “Uses of Positive-Pressure Techniques” on pp. 746 of manual. Point out the various ways to apply positive-pressure ventilation.

#### Types of openings

##### Entry (inlet) opening – Location where fan or blower set up

##### Exhaust opening – Point varies with size of entry opening, capacity of blower, and may be a window or doorway

#### Once an exhaust opening created – Blower placed outside entry opening

##### Normal single 3-foot (0.9 m) wide door, distance between door and fan should be 4 to 6 feet (1.2 to 1.8 m) – Distances may be altered for larger door openings

##### Cone of air must completely cover opening

##### To maintain positive pressure inside – Important to control location, number, size of exterior openings

#### During post fire suppression

##### Can be used to ventilate interior compartments by systematically opening, closing interior doors, exterior windows

##### Process accelerates removal of heat, smoke from building

#### In multistory building

##### Best when applied at lowest point

##### Applied at ground level with one or more blowers

##### Directed throughout by opening, closing doors until smoke evacuated

##### More fans added on upper floors, at entry point if single fan insufficient

##### Smoke systematically removed one floor at time by selectively opening exit points

###### Cross-ventilating floors

###### Directing smoke up stairwell and out rooftop opening

##### Larger blowers available for multi-story, large-volume buildings

Instructor Note: This information correlates with Skill Sheet 13-I-3. More information is found at the end of this lesson outline.

#### Main problem – Coordination of opening, closing doors in stairwell used to ventilate building

#### To control openings or pressure leaks

##### One person in charge of pressurizing process

##### Use portable radios

##### Firefighters patrol stairwell, hallways

#### For effective PPV operation

##### Ensure exhaust opening sufficient to handle air flow

##### Monitor operation of PPV fan

##### Maintain communications between IC, interior attack crews, PPV operator

##### Take advantage of existing wind conditions

##### Make certain cone of air from fan covers entire entry opening

##### Reduce volume of area pressurized by selectively opening, closing interior doors

##### Avoid creating unintended horizontal openings

WARNING! Improperly applied, PPV can change the interior conditions and injure personnel working inside the structure.

### Advantages of PPV compared to NPV

#### PPV blowers can be set up without entering smoke-filled environment

#### PPV equally effective with either horizontal or vertical ventilation because it supplements natural air currents

#### Removal of smoke, heat is more efficient

#### Velocity of air currents is minimal, creates little to no effects that disturb contents or smoldering debris – Total exchange of air within building faster than NPV alone

#### Fans powered by internal combustion engines operate more efficiently in clean air

#### Cleaning, maintenance of fans used for PPV significantly less than those needed for NPV fans

#### PPV effective in all structure types, particularly in large, high-ceiling areas where NPV is ineffective

#### Heat, smoke may be directed away from unburned areas or egress paths

#### Exposed buildings or adjacent compartment can be pressurized, reducing fire spread

### Disadvantages of PPV

#### Structure must be intact

#### Interior carbon monoxide levels may be increased if fan exhaust from fans powered by internal combustion engines is allowed to enter

#### Hidden fires may accelerate, spread throughout building

### Hydraulic ventilation

#### Used where other types of forced ventilation unavailable

##### Used to clear room or building of smoke, heat, steam, gases after fire controlled

##### Uses spray stream from fog nozzle to entrain smoke, gases – Carry out of structure through door or window

###### Fog nozzle set on wide fog pattern to cover 85 to 90 percent of opening where smoke will be drawn

###### Nozzle tip at least 2 feet (0.6 m) back from opening

###### Faster ventilation occurs with larger openings

Instructor Note: This information correlates with Skill Sheet 13-I-4. More information is found at the end of this lesson outline.

#### Disadvantages

##### May increase water damage within structure if done incorrectly

##### Drain on available water supply – Especially crucial in rural operations where water shuttles used

##### In freezing temperatures – Will be increase in amount of ice on ground surrounding building

##### Nozzle operators must remain in heated, contaminated atmosphere throughout operation

##### Operation may have to be interrupted when nozzle team leaves area to replenish air supply

Review Question: What are the main types of horizontal ventilation? 
See pages 744-749 of the manual for answers.

### Precautions against upsetting horizontal ventilation

#### Must take care not to upset effects – Opening door on windward side before creating exhaust on leeward may

##### Pressurize building

##### Intensify fire

##### Cause fire spread

#### Take advantage of air currents established by horizontal ventilation – Obstruction in established currents may reduce or eliminate positive effects

### Advantages of mechanical ventilation

#### Supplements, enhances natural ventilation

#### Ensures more control of air flow

#### Speeds removal of contaminants

#### Reduces smoke damage

#### Promotes good public relations

#### Benefits confined spaces with low oxygen levels

### Disadvantages of improper mechanical ventilation

#### Can cause fire to intensify and spread

#### Depends upon power source

#### Requires special equipment

#### Requires additional resources, personnel

Review Question: How do the advantages and disadvantages of natural, mechanical, and hydraulic ventilation compare to one another? 
See pages 744-751 of the manual for answers.

pp. 751	Objective 7 — Describe the types of vertical ventilation.

## Vertical Ventilation

### Occurs after IC

#### Determined need for ventilation

#### Determined it can be done safely, effectively

#### Considered age and type of construction involved

#### Considered location, duration, extent of fire

#### Observed safety precautions

#### Identified escape routes

#### Selected place to ventilate

#### Moved personnel, tools to roof

### Presents increased risks

#### Placing personnel above ground level

#### Working on both peaked and flat surfaces

#### Working above fire

#### Working on roofs that may have been weakened because of age or fire damage

### IC must assess risks, implement safety precautions, and determine if vertical ventilation must be offensive or defensive

#### Offensive – Aid in reaching, extinguishing fire

#### Defensive – Stop spread of fire and contain it in one area of structure

### Safety precautions

#### Check wind direction and velocity to determine effect on exposures

##### Work with wind at back or side when cutting roof opening

##### Protects from heat, smoke, embers

#### Note obstructions or excessive weight that may contribute to roof collapse

#### Provide secondary means of escape for crews from roof

#### Ensure main structural supports not cut while creating opening

#### Guard opening to prevent personnel from falling into it

#### Evacuate roof promptly when work complete or ordered to leave

#### Use lifelines, roof ladders, other means to prevent personnel from sliding, falling off the roof

#### Make sure roof ladder firmly secured over roof peak before working

CAUTION:  Roof ladders are only meant to prevent slipping and are not intended to be used on fire-weakened roofs.

#### Exercise caution when working around electric wires, solar panels, guy wires

#### Ensure all personnel on roof are wearing full PPE including SCBA and breathing SCBA air

#### Keep firefighters out of range of those swinging axes, operating power saws

#### Remain aware of overhead obstructions within range of swing

#### Start power tools on ground to ensure operation – Shut off before hoisting or carrying to roof

#### When using power saw – Make sure angle of cut is away from body

#### Extend ground ladders at least three to five rungs above edge of roof or top of parapet wall – Secure to wall or roof

#### When operating from aerial ladder platforms – Ensure that floor of platform is even with or slightly above roof level

#### Check roof for structural integrity before stepping onto it, continue sounding throughout operation

#### Both before and after ventilating – Walk on load-bearing walls and strongest points of roof structure whenever possible

#### When roof has been opened – Penetrate ceiling below to enhance ventilation

WARNING!  Never direct a fire stream into a vertical exhaust opening when interior attack crews are inside the structure because it will force smoke, heat, and steam down on them.

### Sounding the roof

#### Should be done

##### Before stepping off ladder, parapet wall, other place of safety onto roof

##### Especially if obscured by smoke or darkness

#### How to perform, what to expect

##### Striking the roof surface with blunt end of pike pole, rubbish hook, axe

##### May feel solid over structural supports – Tool bounces off surface

##### May feel softer, less rigid between supports

##### May sound solid over rafter or joist – Producing hollow sound struck between supports

##### Practice on structurally sound roofs needed to recognize different feeling and sounds of areas

Instructor Note: This information correlates with Skill Sheet 13-I-5. More information is found at the end of this lesson outline.

##### Several layers of composition shingles or other coverings may not respond to sounding

##### Tile or slate roofs cannot be sounded – Must be removed to reveal underlying structure

#### Use preincident planning information to identify buildings with roofs supported by lightweight or engineered trusses – These roofs may fail early in a fire, extremely dangerous to work on or under

#### Warning signs of a possible unsafe roof condition

##### Melting asphalt

##### Spongy roof – Normally solid roof that springs back when walked upon

##### Smoke coming from roof

##### Fire coming from roof

Note: Some roofs are spongy with no fire involvement. Know the roofs in your response area.

Caution: Work in groups of at least two, but with no more personnel than absolutely necessary to perform the assigned task.

### Roof-cutting operations

#### Rotary saws, carbide-tipped chain saws, chain saw with adapted features best for roof-cutting – Faster, less damaging than other tools

#### Saw operator must

##### Have good footing and maintain control of saw at all times

##### Use rubbish hook or Halligan on pitched roof to provide secure foothold

#### Turn off saw during transportation to or from operation point – Especially when moving up or down ladder

Instructor Note: This information correlates with Skill Sheets 13-I-6 and 13-I-7. More information is found at the end of this lesson outline.

### Roof ventilation team should be in constant communication with supervisor or IC with team leader

### Responsibilities of ventilation team leader

#### Ensuring roof is safe – Sounding, visual observation

#### Ensuring only required openings made

#### Directing efforts to minimize secondary damage (damage caused by fire fighting operations)

#### Coordinating team’s efforts with those of firefighters inside building

#### Ensuring safety of all personnel assisting with ventilation operations

#### Ensuring there are two means of egress from roof

#### Ensuring adequate exhaust opening size

#### Ensuring the team leaves roof as soon as their assignment completed

### Before cutting any type of ventilation hole, should cut inspection hole in roof

#### Used to help determine location of fire and direction of fire located in attic or cockloft

#### Used in offensive and defensive operations

### Kerf cut inspection hole easiest, fastest to cut

#### Make single cut using rotary saw, chair saw or axe

#### Hole should be width of saw or axe blade

#### Disadvantage – Fire heat can melt tar or membrane, sealing cut

### Triangle or “A” cut inspection hole – Provides most reliable condition information

#### Created from single kerf cut if conditions indicate need

#### Use rotary or chain saw to cut three overlapping cuts that form triangle or letter “A”

##### First – Diagonal cut from upper left to lower right

##### Next – Diagonal cut from top of first cut to lower left

##### Last – Connect two lower ends of previous cuts

##### Center should fall through – May be necessary to push to free, use tool; NEVER use hand

#### Heated smoke, gases, sometimes fire may exit hole

### Offensive ventilation methods

#### Involves making opening over seat of fire at or near highest point of roof

#### Type of exhaust opening and method used will depend on roof type

#### Two critical points when cutting exhaust opening

##### Square or rectangular opening is easier to cut and repair after fire

##### One large opening at least 4 by 8 feet (1.2 m by 2.4 m) much better than several small ones

### Flat roof

#### Most common type of opening made in flat roof – Square or rectangular

#### Openings made between roof trusses or with truss in middle of opening

#### Use louver cut when truss is in middle of opening

Instructor Note: This information correlates with Skill Sheet 13-I-8. More information is found at the end of this lesson outline.

##### Steps to make louver cut in flat roof

###### Make initial opening no smaller than 4 by 8 feet (1.2 m by 2.4 m) - Exhaust opening may need enlargement

###### Identify location of rafters

###### Make short cuts across top and bottom of rafter; long cuts parallel to either side of rafter

###### Strike near side to break loose from rafters and pull far side toward you with roof hook

### Pitched roof, shingle-covered

#### Cut few inches (mm) below peak on leeward side

#### Always cut exhaust openings at or very near highest point on roof when possible

#### Work from roof ladder with hooks attached to ridge line

#### Work from aerial platform on extremely steep roofs

Instructor Note: This information correlates with Skill Sheet 13-I-9. More information is found at the end of this lesson outline.

### Pitched roof, slate or tile-covered

#### May be attached to solid sheathing or battens with spaces between

#### Open by removing individual pieces or using sledgehammer to smash slate, tile pieces

#### For solid sub roof – Cut hole in manner for pitched roofs

#### Hole may not be needed in battens if enough space between for ventilation

### Arched roofs

#### Same procedure as flat or pitched – Except no ridge to hook ladder

#### Curvature prevents ladder from laying flat

#### Before proceeding – Make kerf cut to locate arches, observe truss space, determine fire involvement

#### Walk on trusses, other strong points only

### Metal roofs

#### Thin metal can be sliced open with axe, carbide tip chain saw, rotary saw and peeled back

#### Thick metal can be opened by metal cutting tool, power saw with metal cutting blades

#### Industrial buildings – Easier, faster to open skylights, monitors, scuttle hatches

#### Older buildings

##### May be large pieces of sheet metal laid over skip sheathing

##### Open with power saw, axe, large sheet-metal cutter

### Defensive ventilation methods

#### Trench cut

##### Strictly defensive

##### NOT to be confused or used as offensive vertical ventilation

##### Used to create fire break to stop fire spread in common attic or large structures

##### Can be time consuming, physically taxing on personnel

##### Works well in large buildings with common cockloft or attic

#### IC decides on defensive stance if fire too great to extinguish – Will abandon efforts to save building

#### To make trench cut – Opening must be created

##### At least 30 feet (9.1 m) ahead of advancing fire,

##### Only after offensive vertical ventilation opening made – Allows

###### Heat and to smoke escape

###### Trench completion before fire front reaches that point

##### If offensive opening not made

###### Fire quickly drawn to and burns past unfinished trench

###### Continues to spread through building while endangering firefighters on roof

#### Created by

##### Making two parallel cuts extending from one exterior wall to other

##### Removing roof material between cuts

##### Pushing ceiling material down

##### Distance between cuts

###### Large enough to prevent fire burning past opening

###### Small enough to not compromise roof integrity

###### Cut of 3 to 4 feet (0.9 to 1.2 m) should be sufficient

Instructor Note: This information correlates with Skill Sheet 13-I-10. More information is found at the end of this lesson outline.

#### Improper trench cut

##### Places firefighters in dangerous position – Working ahead of fire

##### May cause fire to spread more rapidly and potentially destroy entire structure

Review Question: What are the types of vertical ventilation? 
See pages 751-759 of the manual for answers.

#### All members must

##### Plan ahead

##### Establish communications between roof ventilation team and IC

##### Maintain good communications

##### Be aware of the dangers

##### Have clear understanding of objective

##### Have charged hoseline present

##### Wear full PPE and SCBA

##### Have two means of escape from roof that are remote from each other and do not include crossing over cut

##### Assign roof safety officer to observe conditions

##### Cut small inspection holes a few feet from trench on both fire and safe working side

### Precautions against upsetting established vertical ventilation

#### Factors that can reduce effectiveness

##### Improper use of mechanical ventilation

##### Indiscriminant window breaking

##### Fire streams directed at ventilation openings

##### Explosions

##### Burn-through of roof, floor, or wall

##### Additional openings between attack team, upper opening

##### Improper location of vertical ventilation opening

#### Not solution to all ventilation problems

##### May be impractical or impossible

##### Use other strategies when necessary

Warning! Do not direct a fire stream into a ventilation opening during offensive interior operations.

Review Question: What differences are there between horizontal and vertical ventilation? 
See pages 742-759 of the manual for answers.

pp. 760	Objective 8 — Recognize other types of ventilation situations.

## Other Types of Ventilation Situations

### Basement fires

#### Heat, smoke quickly spreads upward into building unless vents installed

#### Access

##### Difficult without effective ventilation

##### Must descend through rising heat, smoke to get to seat of fire

##### May be through interior or exterior stairs, exterior windows, hoistways

##### Outside entrances may be blocked or secured

#### Ventilation accomplished several ways

##### Horizontal ventilation effective if ground-level windows or below ground-level window wells available

##### Interior vertical ventilation used if no ground-level windows available

##### Stairwells, hoistway shafts used to evacuate heat, smoke – Use only if there is means to expel into atmosphere, not endanger other building portions

##### Last resort – Cut opening in floor near ground-level door or window; force heat, smoke from opening through exterior opening using fans

### Fires in windowless buildings

#### Complicate operations

#### Cause delays when creating openings

#### Problems vary depending on

##### Size

##### Occupancy

##### Configuration

##### Construction materials

#### Usually requires mechanical ventilation for smoke removal

##### Can clear smoke through HVAC systems if designed to do so – If not may cause spread of heat, fire

##### HVAC systems should be brought under fire department control prior to fire operations

#### Allow systems to work if designed to contain combustion products, operating properly—if not, IC notified, steps taken to control manually

### High-rise fires

#### Buildings may contain

##### Hospitals, hotels, apartments, offices

##### More occupants – Higher life safety considerations

#### Tactical ventilation must be carefully coordinated

#### Personnel required often four to six times greater than typical low-rise building

#### Fire, smoke, and toxic gases can spread rapidly through pipe shafts, stairways, elevator shafts, unprotected ducts, other vertical or horizontal openings

##### Openings contribute to stack effect

##### Creating upward draft, interfering with evacuation and ventilation

#### Horizontal smoke spread

##### Heated smoke, fire gases travel upward until reaching top of building or cooling to temperature of surrounding air

##### When equalization occurs gases stop rising; will spread horizontally and stratify

#### Hot gas layer development

##### Layers may collect on floors below top floor

##### Additional heat and smoke forces layers to expand, move upward to building top floor

##### May occur when vertical exhaust opening not large enough

#### Tactical vertical ventilation must be considered during preincident planning

##### Usually must be accomplished horizontally with mechanical ventilation, building’s HVAC systems

Instructor Note: Discuss with students the tactical ventilation example for high-rise buildings on pp. 762 of manual. Point out how the different tactics used help address the problems inherent in stratified smoke.

##### Many buildings, only one stairwell penetrates roof

###### Stairwell can be used like a chimney to ventilate smoke, heat, fire gases from various floors

###### Another stairwell used as escape route for occupants

##### During a fire, doors on uninvolved floors must be controlled so occupants do not accidentally enter ventilation stairwell as they are evacuating

###### Before doors on fire floors opened and stairwell ventilated, door leading to roof must be blocked open or removed from its hinges

###### Preventing door at top of shaft from closing ensures it cannot compromise established ventilation operations

##### When ventilating top of a stairwell you are drawing the smoke and heat to you or anyone else in stairwell between fire floor and roof

##### When enclosed secondary stairwell used for evacuating occupants, PPV fans should be located at bottom floor to pressurize stairwell, keep smoke from entering

#### Ventilation fans may be built into top of stairwell to assist

##### Fans draw smoke from fire floor to top when activated

##### Technique may make fire suppression team entry on fire floor from this stairwell difficult

##### May need to pressurize stairwells with PPV fans to confine smoke

Note: Under some conditions, elevator shafts that penetrate the roof may be used for ventilation.

WARNING!  Do not use stairwells or elevator shafts simultaneously for both evacuation and ventilation.

Review Question: What other types of ventilation situations might firefighters encounter? 
See pages 760-763 of the manual for answers.

Section IV: Effects of Building Systems on Tactical Ventilation

# Effects of building systems on tactical ventilation

pp. 763-764	Objective 9 — Explain the effects of building systems on tactical ventilation.

## Effects of Building Systems on Tactical Ventilation

### Modern buildings have HVAC systems – Can contribute to spread of smoke, fire, toxic gases

### Systems usually controlled from panel in maintenance, operations center in basement or at ground level

#### Control panel includes

##### Building duct system diagram

##### Information on smoke detection and fire suppression systems built into HVAC ductwork – Designed shut system down automatically when smoke or fire detected in ducts

#### Firefighters should be familiar with location, operation of controls to shut down HVAC system

### Restoring HVAC system to operation responsibility of building engineer or maintenance superintendent

### Ductwork may create additional fire damage

#### Through heat conduction through metal

#### Check combustibles adjacent to ductwork for possible fires created by conduction

### Built-in smoke control systems

#### Designed to confine fire to smallest area possible by compartmentalizing building when smoke or fire is detected

#### Often used in high-rises, shopping malls, buildings with open atria

#### Methods of compartmentalizing structure – Automatic closing of doors, partitions, windows, HVAC systems

### Smoke control system may include system diagram in same location as control panel

#### Panel should indicate where alarm originated, which automatic closers activated

#### Should only be operated by building engineers or maintenance superintendents

#### Incorrect use can cause severe damage, create more hazardous conditions

WARNING! Do not attempt to operate building systems that assist in ventilation.

Review Question: How can a built-in heating ventilation and air conditioning (HVAC) system affect tactical ventilation? 
See pages 763-764 of the manual for answers.

Section V: Skill Sheets

# SKILL SHEETS

pp. 765	Objective 10 — Ventilate using mechanical negative pressure in a window.

## Skill Sheet 13-I-1

### For this skill sheet, students will perform the skills to ventilate using mechanical negative pressure in a window

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-1 on the curriculum flash drive

### This checklist corresponds with the information on pp. 765 of the manual

pp. 766	Objective 11 — Ventilate using mechanical negative pressure in a doorway.

## Skill Sheet 13-I-2

### For this skill sheet, students will perform skills to ventilate using mechanical negative pressure in a doorway

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-2 on the curriculum flash drive

### This checklist corresponds with the information on pp. 766 of the manual

pp. 767	Objective 12 — Ventilate using mechanical positive pressure.

## Skill Sheet 13-I-3

### For this skill sheet, students will perform skills to ventilate using mechanical positive pressure.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-3 on the curriculum flash drive

### This checklist corresponds with the information on pp. 767 of the manual

pp. 768	Objective 13 — Perform horizontal hydraulic ventilation.

## Skill Sheet 13-I-4

### For this skill sheet, students will demonstrate the skills to perform horizontal hydraulic ventilation.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-4 on the curriculum flash drive

### This checklist corresponds with the information on pp. 768 of the manual

pp. 769	Objective 14 — Demonstrate the procedure for sounding a roof.

## Skill Sheet 13-I-5

### For this skill sheet, students will demonstrate the skills to perform the procedure for sounding a roof.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-5 on the curriculum flash drive

### This checklist corresponds with the information on pp. 769 of the manual

p. 770	Objective 15 — Ventilate using a rotary saw to cut an opening

## Skill Sheet 13-I-6

### For this skill sheet, students will perform skills to ventilate using a rotary Ventilate using a rotary saw to cut an opening saw to cut an opening.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-6 on the curriculum flash drive

### This checklist corresponds with the information on pp. 770 of the manual

p. 771	Objective 16 — Ventilate using an axe to cut an opening.

## Skill Sheet 13-I-7

### For this skill sheet, students will perform skills to ventilate using an axe to cut an opening.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-7 on the curriculum flash drive

### This checklist corresponds with the information on p. 771 of the manual

pp. 772-774	Objective 17 — Demonstrate the procedure for opening a flat roof.

## Skill Sheet 13-I-8

### For this skill sheet, students will perform skills to demonstrate the procedure for opening a flat roof.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-8 on the curriculum flash drive

### This checklist corresponds with the information on pp. 772-774 of the manual

pp. 775-776	Objective 18 — Perform the steps for opening pitched roofs.

## Skill Sheet 13-I-9

### For this skill sheet, students will perform the steps for opening pitched roofs.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-9 on the curriculum flash drive

### This checklist corresponds with the information on pp. 775-776 of the manual

pp. 777-778	Objective 19 — Demonstrate the procedure for making a trench cut using a rotary saw.

## Skill Sheet 13-I-10

### For this skill sheet, students will demonstrate the procedure for making a trench cut using a rotary saw.

### This skill sheet can be found in the Skills Evaluation Checklist 13-I-10 on the curriculum flash drive

### This checklist corresponds with the information on pp. 777-778 of the manual

Section VI: Summary and Review

# SUMMARY AND REVIEW

## Chapter Summary

### Tactical ventilation of a burning building allows heat, smoke, and fire gases to escape to the atmosphere and also draws fresh air into the building.

### Properly applied tactical ventilation allows firefighters to see better, locate victims more easily, and find the seat of the fire sooner.

### Tactical ventilation limits fire spread and channels heat and smoke away from trapped victims; but must be correctly coordinated.

### Firefighters must understand fire behavior, know various ventilation methods and have knowledge of roof construction and know how to create exhaust openings in all types of roofs that have a variety of openings in order to perform ventilation correctly.

## Review Questions

### What are the reasons for tactical ventilation? (732-733)

### What considerations will affect the decision to ventilate? (734-742)

### What are the basic means used to accomplish ventilation? (742-744)

### How do smoke, air flow, heat, and flame impact fire behavior in a structure? (737-738)

### What differences are there between horizontal and vertical ventilation? (744-760)

### How do the advantages and disadvantages of natural, mechanical, and hydraulic ventilation compare to one another? (749-751)

### What are the main types of horizontal ventilation? (744-751)

### What are the types of vertical ventilation? (751-756)

### What other types of ventilation situations might firefighters encounter? (760-763)

### How can a built-in heating ventilation and air conditioning (HVAC) system affect tactical ventilation? (761)